THE UNIVERSITY OF IOWA

DESIGN STANDARDS & PROCEDURES

September 2023 EDITION

PREFERMENT 06

UIHC Restrooms

EFFECTIVE DATE:  April 5, 2024

The information contained in this Preferment modifies, supplements, or replaces information contained in The University of Iowa Design Standards & Procedures.

APPLICABLE SECTION:	Section III – General Design Standards and Outline Specifications and Details

ATTACHMENT(S):	NONE

APPLICABLE TO SECTION III – General Design Standards and Outline Specifications and Details:

ITEM #1	Subsection 2) Space Guidelines

Article 2. Restrooms

ADD the following articles:

2.3.1	For UIHC: Drywall ceilings are permitted in in-patient restrooms.

2.4.1	For UIHC: Hose bibs are not permitted in any UIHC restrooms.

2.7.5	For UIHC: Remodel projects impacting, or adjacent to, existing restroom facilities on the main floor and within the main circulation path shall include an accessible single user restroom where feasible.

2.8.1	For UIHC: Baby changing stations are not required in in-patient restrooms. They may be installed at the owner’s request based on patient population. They shall be installed in public restrooms.

2.13.1 	For UIHC: Full width mirrors are not required.

2.14.1	For UIHC: A narrow shelf is not required near the entrance of the restroom.

2.15.1	For UIHC: Coat hooks are not required near the entrance of the restroom.

2.18.1	For UIHC: Built-in or metal waste receptacles shall not be used unless there are space constraints.

2.19.1	For UIHC: Sharps containers shall only be installed in public restrooms within the main circulation path.  They are not permitted in in-patient restrooms.

2.21.1	For UIHC: Sanitary napkin and tampon dispenser may be installed in restrooms.

2.22.1	For UIHC: All accessible toilet stalls and in patient restrooms shall have side wall vertical grab bars.

2.23.1	For UIHC: The outlet of the toilet paper dispenser shall be below the grab bar.

END OF PREFERMENT